## Slide 1
Predicting EPC Energy Ratings
for Oxford's domestic stock
A leakage-aware ordinal-classification pipeline with SHAP-driven retrofit recommendations
COM6003 • Buckinghamshire New University • 2025-26
Author: Muhammad Omer Hussain (22509495)

## Slide 2
Why this matters
EPCs are the evidence base for retrofit policy and finance
• UK net-zero by 2050 → domestic buildings ≈ 17% of UK emissions (CCC, 2023).
• EPC rating drives lender retrofit lending, MEES enforcement, ECO grant routing.
• Oxford: 30.4% of dwellings built before 1900: almost double the England-wide share (ONS, 2023).
• Question: which physical features drive Oxford's rating, and where should retrofit £ go first?
17%
Domestic share of UK emissions
30.4%
Oxford dwellings built pre-1900
~5
SAP-point inter-assessor variance
COM6003 • Oxford EPC Analysis
2 / 14

## Slide 3
Data
Energy Performance of Buildings Register: Oxford (E07000178)
• Source: DLUHC / MHCLG, EPB Register; OGLv3 + restricted Ordnance Survey / Royal Mail address licence.
• Raw certificates for Oxford: 76430 rows × 93 columns.
• After cleaning + dedup-per-UPRN: 49,442 certificates.
• Two tables linked by LMK_KEY: certificates (one row per lodgement) + recommendations.
• Targets: CURRENT_ENERGY_RATING (ordinal A-G, primary); CURRENT_ENERGY_EFFICIENCY (1-100, secondary).
COM6003 • Oxford EPC Analysis
3 / 14

## Slide 4
Pipeline
Leakage-aware, reproducible, every step a pure function
Typed loader
explicit dtypes, parsed dates
Leakage filter
drop SAP-engine outputs
Dedup-per-UPRN
latest EPC per dwelling
Feature engineering
19 engineered features
ColumnTransformer
fit only on train fold
HistGB regression-to-band
with SAP-cohort routing
SHAP + calibration + fairness
audit every result
Train ≤ 2022-12-31 → Hold-out ≥ 2023-01-01 (temporal split)
COM6003 • Oxford EPC Analysis
4 / 14

## Slide 5
The single biggest pitfall: and how we avoided it
Leakage audit on the SAP-derivative columns
• The target is *derived* from the SAP/RdSAP calculation: many columns in the CSV are *outputs* of the same engine.
DROPPED: would leak
• POTENTIAL_ENERGY_RATING / EFFICIENCY
• ENVIRONMENTAL_IMPACT_*
• ENERGY_CONSUMPTION_*
• CO2_EMISSIONS_*
• LIGHTING_COST_*, HEATING_COST_*, HOT_WATER_COST_*
• Per-element *_ENERGY_EFF stars (kept for diagnostics, not features)
KEPT: physical reality only
• PROPERTY_TYPE, BUILT_FORM, CONSTRUCTION_AGE_BAND
• WALLS_DESCRIPTION, ROOF_DESCRIPTION, WINDOWS_DESCRIPTION
• MAIN_FUEL, MAIN_HEATING_CONTROLS, MAINS_GAS_FLAG
• TOTAL_FLOOR_AREA, NUMBER_HABITABLE_ROOMS, …
• Engineered: FLAG_CAVITY_INSULATED, FLAG_LOFT_300MM, …
• Dedup-per-UPRN: same dwelling never crosses the split
COM6003 • Oxford EPC Analysis
5 / 14

## Slide 6
EDA: what we found
Class imbalance and a clear age-band gradient
COM6003 • Oxford EPC Analysis
6 / 14

## Slide 7
Why?
Walls dominate; age is monotonic; glazing is real but smaller
Test statistics (hold-out)
Spearman ρ: age vs SAP
0.618
Spearman ρ: multi-glaze vs SAP
0.209
Cramér's V: walls vs rating
0.407
Cramér's V: main fuel vs rating
0.318
Cramér's V: age band vs rating
0.366
Cramér's V: built form vs rating
0.091
COM6003 • Oxford EPC Analysis
7 / 14

## Slide 8
Model comparison
Quadratic Weighted Kappa: 5-fold GroupKFold (no UPRN leakage)
Model
QWK
± std
Logistic regression (full)
0.40
Random Forest (group split)
0.840
± 0.003
HistGB classifier (group)
0.840
± 0.002
LightGBM + expected-value
0.867
± 0.005
Regression-to-band (champion)
0.863
Ensemble (RF+HGB+LGBM mean proba)
0.860
COM6003 • Oxford EPC Analysis
8 / 14

## Slide 9
How the champion turns features into a band
Regression-to-band with SAP-cohort routing
EPC bands are a deterministic discretisation of the SAP score, so predicting the score and then thresholding is statistically consistent (Pedregosa et al., 2017) and supports counterfactual retrofit queries a discrete classifier cannot express.
COM6003 • Oxford EPC Analysis
9 / 14

## Slide 10
Champion: SapStratifiedRegressor hybrid
Regression on SAP score + SAP-cohort specialist; evaluated once on inspections from 2023+. Multi-seed: 0.7714 ± 0.0019 across seeds 42/123/2026.
0.7696
Quadratic Weighted Kappa
0.584
Balanced accuracy
0.550
Macro-F1
4.05
SAP MAE (vs ~5-pt assessor noise floor) | 97.7% within 15 SAP pts (ONS DSC national: 93%)
COM6003 • Oxford EPC Analysis
10 / 14

## Slide 11
What drives the rating
Windows, construction age and main fuel dominate by permutation importance
• Windows: single-glazed dwellings carry the largest negative SHAP contributions; multi-glazed the largest positive. Top feature by permutation importance (Δ-QWK +0.071 on shuffle).
• Construction age: monotonic gradient reflecting four decades of Part L revisions (Spearman ρ 0.62 vs SAP).
• Main fuel and heating type: gas / condensing-boiler dwellings score higher; heat pumps do not improve the rating because SAP is cost-based and electricity is ≈ 3× more per kWh.
• Walls: solid-brick uninsulated drives negative SHAP; cavity-with-insulation positive (FLAG_SOLID_BRICK_BARE in top 10).
• Permutation importance and SHAP agree on the top features → robust signal, not algorithmic artefact.
COM6003 • Oxford EPC Analysis
11 / 14

## Slide 12
Unsupervised segmentation and retrofit recommender
Three fabric archetypes (K-Prototypes, k = 3) and an Apriori + content-based k-NN recommender
k = 3
K-Prototypes segments
0.24
Gower silhouette (soft archetypes)
8.9
Top Apriori rule lift
0.97
Recommender hit-rate (precision@5 +0.08 vs popularity)
COM6003 • Oxford EPC Analysis
12 / 14

## Slide 13
Recommendations
For Oxford City Council and registered providers
1.
Solid-wall insulation in pre-1929 stock
Largest single physical lever; £4-14k per dwelling; SAP-engine corroborates.
2.
Loft insulation top-ups to ≥ 270 mm
Cheapest material intervention; positive SHAP across nearly all bands.
3.
Replace single glazing in 1900-1949 cohort
Concentration of FLAG_SINGLE_GLAZED; immediate comfort benefit.
4.
Communicate the heat-pump SAP caveat
SAP is cost-based; tariff differential blunts rating gain: manage expectations.
5.
Geographic targeting: OX1 / OX2 / OX4
Highest density of pre-1900 stock; district-weighted subsidies. Operational deliverable: reports/predictions_oxford.csv (76,400 per-UPRN predictions + confidence proxy).
COM6003 • Oxford EPC Analysis
13 / 14

## Slide 14
Limitations & questions
Honest about the ceiling: not all variance is reducible
Acknowledged ceilings, plus where we now stand
• RdSAP is modelled, not measured: assessor variance ≈ ±5 SAP points (Few et al., 2023; Hardy and Glew, 2019). Our score MAE = 4.05 is at the irreducible label-noise floor.
• Lodgement-event selection bias under-represents long-tenure owner-occupied homes.
• Methodology drift across SAP revisions; mitigated, not eliminated, by the temporal split.
• rt_101 (SAP) cohort holdout QWK = 0.578 despite the hybrid lift: SAP-score predictions cluster near band boundaries (98.8% within 15 SAP pts).
• Findings calibrated to Oxford's pre-1900-heavy stock: do not extrapolate unmodified.
• Address-level fields excluded from the model per GDPR Article 5 minimisation.
Questions?